XP Series

Loudspeaker Management System

User Manual

##### XILICA Audio Design

### Important Safety Instructions

### 1. READ THESE INSTRUCTIONS

### All the safety and operating instructions should be read before the product is operated.

### 2. KEEP THESE INSTRUCTIONS

### The safety and operating instructions should be retained for future reference.

### 3. HEED ALL WARNINGS

### All warnings on the product and in the operating instructions should be adhered to.

### 4. FOLLOW ALL INSTRUCTIONS

### All operating and use of instructions should be followed.

### 5. DO NOT USE THIS APPARATUS NEAR WATER

### Do not use the product near water. For example, near a bathtub, washbowl, kitchen sink, or laundry tub, in a wet basement, or near a swimming pool, and the like.

### 6. CLEAN ONLY WITH DRY CLOTH

Unplug the unit from the wall outlet before cleaning. Do not use liquid cleaners or aerosol cleaners. Use a damp cloth for cleaning.

7. DO NOT BLOCK ANY VENTILATION OPENINGS

Slots and openings in the cabinet back or bottom are provided for ventilation, to ensure reliable operation of the limit and to protect it from overheating. These openings must not be blocked or covered. The openings should never be blocked by placing the product on a bed, sofa, rug, or similar surface. This product should never be placed near or over a radiator or heat source. This product should not be placed in a built-in installation such as a bookcase or rack unless proper ventilation is provided or the manufacture's instructions have been adhered to.

8. DO NOT INSTALL NEAR ANY HEAT SOURCES

This Product should be situated away from heat sources such as radiators, stoves, or other products (including amplifiers) that produces heat.

9. DO NOT DEFEAT THE SAFETY PURPOSE OF THE POLARIZED OR GROUNDING-TYPE PLUG

A Polarized plug has two blades with one wider than the other. A grounding-type plug has two blades and a third grounding prong. The wide blade or the third prongs are provided for your safety. If the provided plug does not fit into your outlet, consult an electrician for replacement of the obsolete outlet.

10. PROTECT THE POWER CORD FROM BEING WALKED ON OR PINCHED PARTICULARLY AT PLUGS, CONVENIENCE RECEPTACLES, AND THE POINT WHERE THEY EXIT FROM THE APPARATUS.

11. ONLY USE ATTACHMENTS/ACCESSORIES SPECIFIED BY THE MANUFACTURER.

12. USE ONLY WITH CART, STAND, TRIPOD, BRACKET, OR TABLE SPECIFIED BY THE MANUFACTURER, OR SOLD WITH THE APPARATUS. WHEN A CART IS USED, USE CAUTION WHEN MOVING THE CART/APPARATUS TO AVOID INJURY FROM TIP-OVER.

Do not place this unit on an unstable cart, stand, tripod, bracket, or table. The unit may fall, causing serious injury to someone, and serious damage to the appliance. A unit and cart combination should be moved with care. Quick stops, excessive force, and uneven surfaces may cause the product and cart combination to overturn.

13. UNPLUG THIS APPARATUS DURING LIGHTNING STORMS OR WHEN UNUSED FOR LONG PERIODS OF TIME.

For added protection for this unit during a lightning storm, or when it is left unattended and unused for long periods of time, unplug it from the wall outlet and disconnect the antenna or cable system. This will prevent damage to the unit due to lightning and power line surges.

14. REFER ALL SERVICING TO QUALIFIED SERVICE PERSONNEL. SERVICING IS REQUIRED WHEN THE APPARATUS HAS BEEN DAMAGED IN ANYWAY, SUCH AS WHEN THE POWER SUPPLY CORD OR PLUG IS DAMAGED, LIQUID HAS BEEN SPILLED OR OBJECTS HAVE FALLEN INTO THE APPARATUS, THE APPARATUS HAS BEEN EXPOSED TO RAIN OR MOISTURE, DOES NOT OPERATE NORMALLY, OR HAS BEEN FROPPED.

15. WARNING: TO REDUCE THE RISK OF FIRE OR ELECTRIC SHOCK, DO NOT EXPOSE THIS APPARATUS TO RAIN OR MOISTURE.

16. APPARATUS SHALL NOT BE EXPOSED TO DRIPPING OR SPLASHING AND NO OBJECTS FILLED WITH LIQUIDS, SUCH AS VASES, SHALL BE PLACED ON THE APPARATUS.

### Table of Contents

Table of Contents	4

1.0	Introduction	5

2.0	Features	6

3.0	Front Panel Functions	7

4.0	Rear Panel Functions	9

5.0	Powering Up the Device	10

6.0	Operating the Channel Menus	11

7.0	Operating the System Menus	18

8.0	Quick Reference	25

9.0	PC Control Software	26

10.0	Specifications	27

11.0	Warranty	29

### 1.0	Introduction

The XP series is a digital loudspeaker management system designed for the touring or fixed sound installation markets. The absolute latest in available technology is utilized with 40-bit floating point processors and high performance 24-bit Analog Converters. The high-bit DSP prevents noise and distortion induced by truncation errors of the commonly used 24-bit fixed-point devices. A complete set of parameters include I/O levels, delay, polarity, 8 bands of EQ per channel, 31 bands of GEQ per input, multiple crossover selections and full function limiters. Precise frequency control is achieved with its 1 Hz resolution. Inputs and outputs can be routed in multiple configurations to meet any requirement. The XP series can be controlled or configured in real time on the front panel or with the intuitive PC GUI accessed via the RS-232, USB or Ethernet interface. Software upgrade for CPU and DSP via PC keeps the device current with newly developed algorithms and functions once available. Multiple setup storage and system security complete this professional package.

### Shipped contents:

### - XP Unit

### - User Manual

### - XConsole Software CD

- Power Cord

### 2.0	Features

### >	Up to 8 Inputs and 8 Outputs with flexible routing

### >	40-bit floating point DSP

### >	96kHz Sampling Rate

### >	High Performance 24-bit A/D Converters

### >	1 Hz Frequency Resolution

### >	8 Equalizers (Magnitude or Phase) for each Input and Output

### >	31 Bands GEQ for each Input

### >	Multiple Crossover types with Full Function Limiters

### >	Precise Level, Polarity and Delay

### >	CPU and DSP upgrade via PC

### >	Individual Channel Buttons with Linking capability

### >	2-Line x 16 Character Backlit LCD Display

### >	Full 5-segment LED’s on every Input and Output

### >	Storage of up to 30 Preset Setups

### >	Security Lock

### >	Ethernet, USB and RS232 Interface for PC Control and Configuration >	Mic Preamps + Phantom Power for each Input Channel

### 3.0	Front Panel Functions

- USB – a standard Type B USB connector. Device driver from the provided software CD must be installed prior to usage.

- RS232 – a standard female DB9 socket. A straight through cable is required for PC connection.

- Mute (Channel Menu) Buttons – Mute or un-mute input and output channels. When an input channel is muted, a red LED will come on for indication.

When the <<Menu or Menu>> key is held down, the Mute Buttons selects the corresponding channel for the LCD menu display and is acknowledged by a green LED below the button. The last modified menu will be displayed on the LCD.  Multiple channels can be linked or unlinked by pushing the desired channels. This eases programming for same parameters across multiple channels. Multiple Inputs can be linked together and multiple outputs can be linked together. Inputs and Outputs are linked separately.

- Channel Menu LED – Indicates the activated channels for data modification.

- Peak Level LED – Indicates the current peak level of the Signal:

Signal, -12dB, -6dB, -3dB, Over/Limit. The Input Limit LED references to the device's maximum headroom. The Output Limit LED references to the threshold of the output limiter.

- LCD – Shows all the necessary information to control the unit.

- Menu Buttons – There are 6 menu keys: <<Menu (Menu Down), Menu>> (Menu Up), <<Cursor (Cursor Down), Cursor>> (Cursor Up), Enter/Sys/Speed, Exit.  The functions of each key is explained below:

<<Menu:	Go to previous menu screen.  Holding this button down while pressing Mute key will go to the specify channel menu.

Menu>>:	Go to next menu screen.  Holding this button down while pressing Mute key will go to the specify channel menu.

<<Cursor:		Go to previous cursor in the menu screen.

Cursor>>:		Go to next cursor in the menu screen.

Enter/Sys/Speed:	Enter is used only in the System Menu to proceed with selected actions.

Sys enters the System Menu from the main menu.

Speed modifies delay and frequency (1 Hz resolution mode) data values by 100X.

Exit:			Exit to the Main Menu.

- Rotary Thumb Wheel – Changes parameter data values. The wheel has travel velocity sensing which ease large incremental data modifications. For modifying delay and frequency (1 Hz resolution), pressing the Speed key simultaneously will increment/decrement the data value by 100X.

### 4.0	Rear Panel Functions

- Main Power – Connects via a standard IEC socket. A compatible power cord is supplied with the unit. The voltage input is 90-240VAC, 50-60Hz.

- Main Fuse – T2.5A-250V. Slow blow type.

- Power switch – Controls power On/Off.

- Ethernet – RJ45 connector for Ethernet control.  The device should be connected to a router/switch/hub via a straight through CAT-5 cable.

- Analog Inputs and Outputs – Separate 3-pin connectors are provided for each audio input and output. The device's output stage employs the balanced impedance topology. All I/O connectors have pin 1 as ground (shield), pin 2 as + and pin 3 as -.

### 5.0	Powering Up the Device

- After powering up the unit, the following initialization screen is displayed on the LCD:

- The initialization process takes several seconds and during that period the unit boots and displays the device model and firmware version.

- After the initialization process is finished the XP displays its main screen:

- The screen shows the current program number and program name assigned to the unit. If the program number is 31 and the name is MEMORY, it means that no program is assigned, the last data before previous power down is recalled instead.

- Now the XP is ready to operate.

### 6.0	Operating the Channel Menus

Channel Linking – While holding down the <<Menu or Menu>>, more than 1 channel from the same group (Input or Output group) can be selected to link the channels together. The green LEDs below the Mute buttons are lit for the linked channels. Any modification of the data for the selected channel will be applied to the linked channels as well. To cancel the linking, simply deselect the desired channel while the <<Menu or Menu>> key is still pressed, or just press the Exit key to deselect all channels.

#### 6.1	Input Microphone Gain

LEVEL:

The level (or gain) ranges from 0dB to +45dB in 3dB steps.  This level will only have an affect on the input channel when Mic Input is selected from the System Menu.  Please refer to page 22 for more details.

#### 6.2	Input/Output Signal

LEVEL:

The level (or gain) ranges from -40.00dB to +15.00dB in 0.25dB steps.

POL:

The polarity (or phase) can be normal (+) or inverted (-).

DELAY:

The maximum delay permitted is 650ms, in steps of approximately 10us.  It can be displayed in ms, ft or m.  The time unit of the delay is set in the System Menu.  Please refer to page 21 for more details.

#### 6.3	Input/Output Equalizer

EQ#:

Each input channel has 8 bands of equalization.  This control selects one of the 8 available bands.

BYPASS:

This control will un-bypass (Off) or bypass (On) the currently selected band.

TYPE:

The 5 types of EQ that can be used are: parametric (PEQ), low shelf (LO-SHF), high shelf (HI-SHF), 1st degree all-pass (AP-1), and 2nd degree all-pass (AP-2).

FREQ:

The EQ center frequency ranges from 20Hz to 30kHz in either 1Hz steps or 1/36 octave steps. The frequency steps can be selected in the System Menu.  Please refer to page 21 for more details.

BW:

The EQ bandwidth ranges from 0.02 to 3.61 octaves in steps of 0.01 octave.  The equivalent Q value is automatically shown besides the octave value.  For 1st degree all-pass (AP-1) filter, the bandwidth will sets the phase shift at the centre frequency.  This phase shift is gradually changed from 180 degrees above the centre frequency to the specified value.

LEVEL:

The EQ level (or gain) ranges from -30.00dB to +15.00dB in 0.25dB steps.

6.4	Input Graphic Equalizer

GEQ#:

The graphic equalizer has 31 bands of equalization from 20Hz to 20kHz.  This control selects one of the 31 available bands.  The frequency corresponding to each band is also shown.

LEVEL:

The GEQ level (or gain) ranges from -30.00dB to +15.00dB in 0.25dB steps.

BYPASS:

This control will un-bypass (Off) or bypass (On) the entire GEQ for this channel.

6.5	Input/Output Crossover

TYPL:

The 3 available filter types for the low frequency crossover point (high pass) are: Butterworth, Linkwitz Riley or Bessel.

FRQL:

The filter cut-off frequency for the low frequency crossover point (high pass) ranges from 20 to 30kHz in either 1Hz steps or 1/36 octave steps. The frequency steps can be selected in the System Menu.  Please refer to page 21 for more details.

SLPL:

The filter slope for low frequency crossover point (high pass) ranges from 6 to 48dB/octave. If the selected filter type is Linkwitz Riley, the available slopes are 12, 24, 36 or 48 dB/octave only.

TYPH:

The 3 available filter types for the high frequency crossover point (low pass) are: Butterworth, Linkwitz Riley or Bessel.

FRQH:

The filter cut-off frequency for the high frequency crossover point (low pass) ranges from 20 to 30kHz in either 1Hz steps or 1/36 octave steps. The frequency steps can be selected in the System Menu.  Please refer to page 21 for more details.

SLPH:

The filter slope for high frequency crossover point (low pass) ranges from 6 to 48dB/octave. If the selected filter type is Linkwitz Riley, the available slopes are 12, 24, 36 or 48 dB/octave only.

| Filter configuration | Low crossover point | High crossover point |  |
| --- | --- | --- | --- |
| None | FTRL Off | FTRH Off |  |
| Highpass | FTRL not Off | FTRH Off | FRQL |
| Lowpass | FTRL Off | FTRH not Off | FRQH |
| Bandpass | FTRL not Off | FTRH not Off | FRQL FRQH |

6.6	Input Compressor

THRESH:

The compressor threshold ranges from -20 to +20dBu in 0.5dB steps.

ATTACK:

The compressor attack time ranges from 0.3 to 1ms in 0.1ms steps, then ranges from 1 to 100ms in 1ms steps.

RELEASE:

The compressor release time can be set at 2X, 4X, 8X, 16X or 32X the attack time.

RATIO:

The compressor ratio is the slope in which the signal is compressed. It ranges from 1:1 to 1:40.

6.7	Input/Output Channel Name

NAME:

A 6 characters name can be assigned to each channel.

#### 6.8	Output Limiter

THRESH:

The limiter threshold ranges from -20 to +20dBu in 0.5dB steps.

ATTACK:

The limiter attack time ranges from 0.3 to 1ms in 0.1ms steps, then ranges from 1 to 100ms in 1ms steps.

RELEASE:

The limiter release time can be set at 2X, 4X, 8X, 16X or 32X the attack time.

#### 6.9	Output Source

IN1-8:

This sets the input channel source for the current output channel.  It can be used to mix the input source (in dB) or disable it (Off).  If more than one input sources are enabled, they will be added together as the source for the current output channel.

#### 7.0	Operating the System Menus

The System Menus allow the user to control and change parameters that are related to the system behavior and general operation. It can be accessed by pressing the Sys key in the main menu (when no Input/Output or System Menu is activated). All System Menus require pressing the Enter key to confirm and save the settings.

#### 7.1	Preset Recall

The XP has a built in non-volatile memory that can store up to 30 different preset setups.

P:

This control selects which program to recall from the non-volatile memory. The program name is displayed to the right of the program no.

#### 7.2	Preset Store

The XP has a built in non-volatile memory that can store up to 30 different preset setups. A program can be stored using this menu. The old program with the same program number will be replaced. Once the program is stored in the flash memory, it can be recalled at a later time, even after power down.

P:

This control selects which preset location in the non-volatile memory to be saved.

NAM:

A descriptive name of up to 12 characters can be assigned to each program.

#### 7.3	Mic Settings

An optional microphone preamp can be added to the XP series.  The user can select Line input or Mic input from this menu.  The microphone preamp also comes with Phantom Power, which can also be enabled or disabled here.

IN1-8:

The user can choose between Line input or Mic input.  For Mic input, the input will receive a 30dB gain.  Each input channel can be selected individually.

#### 7.4	Phantom Power

#### The option microphone preamp also comes with Phantom Power, which can also be enabled or disabled from this menu.

IN1-8:

#### A 48V DC voltage can be supplied to external microphone when the Phantom Power is enabled.  Phantom Power cannot be enabled indivually for each input channel, all Mic input channel will automatically receive at 48V DC voltage.  This will not affect Line input since they are disconnected physically.

#### 7.5	Device Configuration

MODE:

The unit assigns the Input source for the corresponding outputs when the Mode of Operation is changed. The crossover point parameters like the filter type, cut-off frequency and slope have to be configured manually in the Crossover Menu for each Output Channel.

| Mode: | Out 1 | Out 2 | Out 3 | Out 4 | Out 5 | Out 6 | Out 7 | Out 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| None | Any | Any | Any | Any | Any | Any | Any | Any |
| Stereo 2-Way | In1 | In1 | In2 | In2 | Any | Any | Any | Any |
| Stereo 3-Way | In1 | In1 | In1 | In2 | In2 | In2 | Any | Any |
| Stereo 4-Way | In1 | In1 | In1 | In1 | In2 | In2 | In2 | In2 |

*Note: The configuration mode configures the input sources when selected. The user can change the source afterwards if desired. It does not keep the configuration in memory.

#### 7.6	Copy Channels

Copy Channels from the source to the target. When the Source and Targets are both Inputs and Outputs, all audio parameters will be copied. When one of the Source or the Target is an input while the other is an output, only the Level, Polarity, Delay, EQ, Crossover, and Channel Name are copied.

SOURCE:

This is the channel to be copied from.

TARGET:

This is the channel to be copied to.

#### 7.7	General Settings

FREQ MODE:

This changes the frequency control mode for EQ and crossover filters.  It can be 36 steps/octave or All Frequencies (1 Hz resolution).

DELAY UNIT:

This sets the time unit for input and output delay to ms, ft, or m.

#### 7.8	Ethernet Settings

The network settings are separated into 3 menus.

Eth-IP:

A unique IP address should be assigned to each unit in the network.

Eth-GW:

The gateway address of the network. Usually, this should be the IP address of your router/switch/hub address.

Eth-SM:

The sets the subnet mask used by your network.

#### 7.9	Communication Settings

NOTE:  User must power cycle the unit for this settings to take effect.

BAUD RATE:

The sets the baud rate of the serial communication.  XConsole uses a baud rate of 115200, it should be left unchanged for most user.

DEVICE ID:

This control assigns a device ID from 1 to 16 to the unit.  This ID is only useful when a network of more than 1 unit is used in conjunction with 1 or more XPanel.

NETWORK ID:

This control assigns a network ID from 0 to 60000 to the unit.  This ID is used for future network expansion only, please leave it at 0.

#### 7.10	Security Password

The factory default password is blank (“____”), it can be changed to any combination of 4 characters in this menu.

OLD PW:

The user is required to enter the old password first to modify the password.

NEW PW:

The new password desired.

#### 7.11	Security Lock

The XP enables the user to secure the unit and prevent undesired changes in the setup. In order to lock or unlock the unit the user must enter the correct password.  The user can only lock or unlock all menus using the front panel, XConsole is required to lock or unlock individual menu.

PASSWORD:

The password is 4 characters in length.  The factory default of a new unit does not require a password.  The user can change the password via XConsole or the Set Password menu.

### 8.0 Quick Reference

| Parameters | Menu <<Menu>> | Field <<Cursor>> | Min | Max | Steps | Units |
| --- | --- | --- | --- | --- | --- | --- |
| Mic Level | Mic | LEVEL | 0 | +45 | 3 | dB |
| Level | Signal | LEVEL | -40 | +15 | 0.25 | dB |
| Polarity | Signal | POL | + / - |
| Delay | Signal | DELAY | 0 | 62400 | 1 | 10us steps |
| EQ Number | EQ | EQ# | 1 | 8 | 1 |  |
| EQ Bypass | EQ | BYPASS | Off /On |
| EQ Type | EQ | TYPE | PEQ / Lo-Shf / Hi-Shf / AP-1 / AP-2 |
| EQ Level | EQ | LEVEL | -30 | +15 | 0.25 | dB |
| EQ Frequency | EQ | FREQ | 20 | 30,000 | 1 | Hz |
| EQ Bandwidth | EQ | BW | 0.02 | 3.61 | 0.01 | Octave |
| GEQ Number | GEQ | GEQ# | 1 | 31 | 1 |  |
| GEQ Level | GEQ | LEVEL | -30 | +15 | 0.25 | dB |
| GEQ Bypass | GEQ | BYPASS | Off / On |
| XOver Low Type | XOver | FTRL | Off / Butterworth / Linkwitz-Riley / Bessel |
| XOver Low Frequency | XOver | FRQL | 20 | 30,000 | 1 | Hz |
| XOver Low Slope | XOver | SLPL | 6 | 48 | 6 | dB/octave |
| XOver High Type | XOver | FTRH | Off / Butterworth / Linkwitz-Riley / Bessel |
| XOver High Frequency | XOver | FRQH | 20 | 30,000 | 1 | Hz |
| XOver High Slope | XOver | SLPH | 6 | 48 | 6 | dB/octave |
| Compressor Threshold | Comp | THRESH | -20 | +20 | 0.5 | dBu |
| Compressor Attack Time | Comp | ATTACK | 0.3 | 100 | 0.1 / 1 | ms |
| Compressor Release Time | Comp | RELEASE | 2 / 4 / 8 / 16 / 32X Attack time |
| Compressor Ratio | Comp | RATIO | 1:1 to 1:40 |
| Limiter Threshold | Limit | THRESH | -20 | +20 | 0.5 | dBu |
| Limiter Attack Time | Limit | ATTACK | 0.3 | 100 | 0.1/1 | ms |
| Limiter Release Time | Limit | RELEASE | 2 / 4 / 8 / 16 / 32X Attack time |
| Source | Source | 1, 2, 3, 4, 5, 6, 7, 8 | Off | +15 | 0.25 | dB |
| Channel Name | Name | NAME | 6 characters |

### 9.0	PC Control Software

The XP series is shipped with a special PC Graphic User Interface (GUI) application - XConsole. XConsole gives the user an option to control the unit from a remote PC via the serial communication link. The GUI application makes it much easier to control and monitor the device, allowing the user to get the whole picture on one screen. Programs can be recalled and stored from/to PC’s hard drive, thus expanding the storage to become virtually limitless.

XConsole can be connected to the XP series via RS232, USB or Ethernet.  USB requires the installation of additional driver.  The user is given an option to install it during the installation of XConsole, and if the user did not install it at that time, they may choose to do so by running the USB driver installer from the provided software CD.

### 10.0	Specifications

Inputs and Outputs

Input Impedance: 	>10k Ohms

Output Impedance:	50 Ohms

Maximum Level: 		+20dBu

Type: 			Electronically balanced

Audio Performance

Frequency Response:	+/- 0.1dB (20 to 30kHz)

Dynamic Range: 		115dB typ (unweighted)

CMMR: 			> 60dB (50 to 10kHz)

Crosstalk:			< -100dB

Distortion:			0.002% (1kHz @+4dBu)

Digital Audio Performance

Processor: 			40-bit

Sampling Rate: 		96kHz

Analog Converters: 	High Performance 24-bit

Propagation Delay: 	1.5ms

Front Panel Controls

Display:			2 x 16 Character Backlit LCD

Level Meters:		5 segment LED

Buttons:			Mute/Edit Controls

Menu Controls

Dial Encoder:		Embedded Thumb Wheel

Connectors

Analog Inputs:		3-pin Female XLR

Analog Outputs:		3-pin Male XLR

RS-232:			Female DB-9

USB:				Type B

Power:			Standard IEC Socket

General

Power: 			90-240 VAC (50-60Hz)

Dimensions: 		19”x1.75”x9” (483x44x229 mm)

Weight: 			10 lbs / 4.5 kg

Audio Control Parameters

Mic Gain:			0to +45dB in 3dB steps

Gain:				-40 to +15dB in 0.25dB steps

Polarity: 			+/-

Delay:			Up to 650ms per I/O

Equalizers (8 per I/O)

Type: 			Parametric, Hi-shelf, Lo-shelf, Phase 1, Phase 2

Gain: 			-30 to +15dB in 0.25dB steps

Bandwidth: 		0.02 to 3.61 octaves (Q=0.3 to 72)

31-Band Graphic Equalizers (1 per Input)

Gain: 			-30 to +15dB in 0.25dB steps

Crossover Filters (2 per I/O)

Filter Types: 		Butterworth, Bessel, Linkwitz Riley

Slopes: 			6 to 48dB/oct

Limiters (1 per Output)

Threshold: 			-20 to +20dBu

Attack: 			0.3 to 100ms

Release: 			2 to 32X the attack time

System Parameters

No. of Presets:		30

Program Names:		12 character length

Delay Units: 		ms, ft, m

Frequency Modes:	36 steps/oct, 1Hz resolution

Note: Specifications subject to change without notice

11.0	Warranty

The XP Series is warranted covering materials and workmanship for a period of five (5) years, as determined by the date of retail purchase (according to the sales receipt from an authorized dealer) or the date of manufacture if the sales receipt is not available (according to the serial number). This warranty applies to the product; therefore, the remainder of the warranty period will be automatically transferred to any subsequent owner. This warranty applies only to failure of a Xilica product caused by defects in materials and workmanship during the stated warranty period. It does not apply to a unit that has been subjected to abuse, accident, modification, improper handling/installation, or repairs made without factory authorization or by anyone other than authorized Xilica Field Service Stations. This warranty is void if the serial number has been defaced, altered or removed. Products covered by this warranty will be repaired or replaced at the option of Xilica, without charge for materials or labor, provided all the terms of this warranty have been met.

For factory service, please call or email for a Return Authorization (R/A) number before shipping. If the product is shipped, the following information must be included in the package:

1. Owner’s complete name, daytime phone number, return street address and return authorization number.

2. The serial number of the product being returned and a copy of the retail sales receipt, if possible.

3. A complete description of the problem(s) experienced, including a brief description of how the equipment is being used and other equipments involved.

XP User Manual v2.03 (Jul 2008)

XILICA Audio Design

www.xilica.com

# Footnotes

For XP-2040M / 3060M / 4080M / 8080M only.

XLR connectors for XP-2040 / 3060 / 4080, Euro Connectors for XP-8080

For XP-2040M / 3060M / 4080M / 8080M models only.

Number of Inputs is dependent on the model.

For XP-2040M / 3060M / 4080M / 8080M only, applies to Phantom Power as well.

The latest version of XConsole and USB driver are available at www.xilica.com.

3-pin Euro Block for XP-8080 model

3-pin Euro Block for XP-8080 model

# Text boxes

I1:______ EQ1

EQ#:1

3

4

I1:______ EQ1

TYPE:PEQ

I1:______ EQ1

BW:0.33 Q=4.36

I1:______ EQ1

FREQ:1000Hz

I1:______ Name

NAME:______

I1:______ EQ1

LEVEL:0.00dB

I1:______ Signal

DELAY:000.000ms

I1:______ Signal

POL:+

** XILICA  XP **

P01 ____________

O1:______ XOver

TYPL:Off

I1:______  GEQ1

BYPASS:Off

O1:______ Limit

ATTACK:10ms

SYSTEM    Passwd

OLD PW:____

SYSTEM    Config

MODE:None

O1:______ Limit

THRESH:+20.0dB

SYSTEM     Store

NAM:____________

SYSTEM     Store

P:1

SYSTEM    Comm

NETWORK ID:0

SYSTEM    Secure

PASSWORD:____

SYSTEM      Copy

TARGET:In2

** XILICA  XP **

XP-4080   v7.08B

I1:______ Signal

LEVEL:0.00dB

SYSTEM      Copy

SOURCE:In1

SYSTEM    Generl

FREQ MODE:All

1,2,3

O1:______ XOver

FRQL:1000Hz

1

O1:______ Source

IN1:Off

O1:______ Source

IN2:-14.00

I1:______  GEQ1

LEVEL:0.00dB   f=20

SYSTEM    Comm

DEVICE ID:1

2

6

5

8

7

I1:______ EQ1

BYPASS:Off

SYSTEM    Generl

DELAY UNIT:ms

I1:______  GEQ1

GEQ#:1   f=20

SYSTEM    Recall

P:1 ____________

4

SYSTEM    Comm

BAUD RATE:115200

5

O1:______ XOver

SLPL:24dB

O1:______ XOver

TYPH:Off

O1:______ XOver

FRQH:1000Hz

O1:______ XOver

SLPH:24dB

O1:______ Comp

THRESH:+20.0dB

O1:______ Comp

ATTACK:10ms

O1:______ Comp

RELEASE:8XAtck

O1:______ Comp

RATIO: 1:1

SYSTEM    Passwd

NEW PW:____

SYSTEM    Eth-SM

:255.255.255.255

SYSTEM    Eth-GW

:255.255.255.255

SYSTEM    Eth-IP

:255.255.255.255

I1:______ EQ1

DEG:15.5 deg

SYSTEM    Phantm

IN1:On

I1:______ Mic

LEVEL:0dB

SYSTEM    Mic

IN1:Line

O1:______ Limit

RELEASE:8XAtck